## Slide 1
EEG-fMRI · MNE-PYTHON · MACHINE LEARNING
Reproducing the
EEG-fMRI pipeline in Python
A faithful reproduction of an EEGLAB preprocessing pipeline, adding a machine-learning component for ICA-component classification, and a quantitative EEGLAB-to-Python validation.
Author Aymen Khatrani
Laboratory MIMLAB, Boğaziçi University
Supervisor Prof. Pınar S. Özbay
ISIA tutor C. Dhaenens

## Slide 2
CONTEXT & PROBLEM STATEMENT
Recording EEG inside the scanner: a signal buried under artifacts
TWO COMPLEMENTARY MODALITIES
EEG brings temporal precision (milliseconds), functional MRI spatial precision (millimeters). Recording them simultaneously combines the best of both.
THE PRICE TO PAY
Inside the scanner, the EEG is contaminated by the gradient artifact (~1 mV, i.e. x1000 the useful EEG) and the pulse / BCG artifact linked to the heartbeat.
Cleaning is classically done in EEGLAB (MATLAB, FMRIB plugin) — proprietary, manual, poorly reproducible. Can we redo it in Python, open and reproducible?

## Slide 3
GOALS & OBJECTIVES
Reproduce, validate, and go further
O1 · REPRODUCE
Recode from scratch each EEGLAB step in Python/MNE, including FASTR (gradient) and OBS (BCG), absent natively from MNE.
O2 · BUILD AN ML DATASET
Extract features describing the ICA components and label them.
O3 · MODEL
Select and optimize a component classifier, compared to ICLabel (domain reference).
O4 · VALIDATE
Quantitatively compare EEGLAB and Python: spectrum, wavelets, ICA topographies, statistics.
ISIA competencies covered: advanced scientific knowledge · building learning datasets · model selection and optimization.

## Slide 4
DATA
Subject sub-38 — resting state, inside the scanner
32
channels (31 EEG 10-20 + 1 ECG)
5000 Hz
sampling rate
~392 s
duration per recording
2
runs (run-01, run-02)
The notebook also runs on a simulated dataset (1/f + alpha EEG, ECG, injected gradient artifact): runnable without real data, for demonstration and testing.

## Slide 5
OVERVIEW
The processing chain, step by step
1.2
Trigger detection fMRI volume marker, data-driven
1.3
Gradient artifact — AAS in-house, FASTR-style
1.4
50 Hz notch filter mains power
1.5
QRS detection heartbeat landmarks (ECG)
1.6
Pulse artifact — OBS in-house, 4-component basis
1.7–1.9
Resampling 250 Hz · average ref · band-pass 1-40 Hz
1.10
ICA — extended Infomax equivalent of runica
1.11–1.12
ICLabel · artifact removal · reconstruction

## Slide 6
PHASE 1 · STEPS 1.2–1.3
Triggers & gradient artifact (AAS)
DATA-DRIVEN DETECTION
The volume trigger is identified from the marker periodicity (coefficient of variation), without reading the docs — hence generalizable.
Result: R128, TR ≈ 3 s, 120 volumes.
AAS — ALLEN 2000
The artifact is repetitive and synchronized: it is averaged over a sliding window of 30 occurrences then subtracted. In-house equivalent of FASTR.
Before: ~1 mV bursts phase-locked to the volume. After: back to the µV range. Assumption: stationarity over the window (else residuals, handled next).

## Slide 7
PHASE 1 · STEPS 1.5–1.6
Pulse artifact — QRS + OBS
WHY THE ECG
The BCG is a mechanical consequence of the heartbeat: the ECG provides the precise timing (R-peak) at which to model the artifact.
767 beats detected (~117 bpm).
OBS — NIAZY 2005
Unlike the gradient, the BCG shape varies from beat to beat. Optimal basis = mean artifact + 4 principal components (SVD), projected then subtracted.
In-house equivalent of pop_fmrib_pas mode 'obs' — recoded from scratch, MNE having no native OBS.

## Slide 8
PHASE 1 · STEPS 1.7–1.12
Filters, ICA and classification
1
Resampling 250 Hz after AAS/OBS (full resolution), before ICA (reduced cost).
2
Average reference ECG excluded; loss of one rank → 30 ICA components.
3
Band-pass 1-40 Hz 1 Hz stabilizes ICA; 40 Hz cuts EMG and gradient residual.
4
ICA extended Infomax reproduces runica; non-deterministic (hence the structural comparison in Phase 2).
5
ICLabel 5 of 30 components flagged as artifact (blinks, muscle); conservative rejection.

## Slide 9
PHASE 2
EEGLAB vs Python: measure, do not assume
SPECTRUM — WELCH
PSD in dB; correlation + mean absolute error against the spectopo export. The signal follows the 1/f decay.
TIME-FREQUENCY — MORLET
Morlet wavelets (= newtimef). Align number of cycles, frequencies and baseline.
ICA — STRUCTURAL
Match topographies by absolute spatial correlation (ICA is not deterministic).
STATISTICS
Wilcoxon, permutation, FDR correction — the lab's inference chain (demo, to aggregate multi-subject).

## Slide 10
PHASE 3 · MACHINE LEARNING
Our own ICA-component classifier
1
12 features / component spectral (band power, peak, 1/f slope), temporal (kurtosis, skewness), spatial (topography entropy).
2
Labeling via ICLabel (cheap labels, but cap performance at 'imitate ICLabel').
3
Synthetic data 300 components generated for training; the 30 real ones reserved for testing.
4
4 model families logistic regression, random forest, SVM, gradient boosting — GridSearchCV, 5-fold cross-validation.
5
Benchmark agreement with ICLabel via Cohen's kappa.

## Slide 11
PHASE 3 · KEY RESULT
An overfitting unmasked
Naive version (misleading)
Test AUC
0.999
Kappa vs ICLabel
0.71
Data leakage + trivial synthetic test set. Inflated scores.
Corrected protocol (honest)
Synthetic AUC
1.00
Real AUC (OOS)
0.50–0.67
Kappa vs ICLabel
0.067
Trained on synthetic only, tested on real components never seen.
The model overfit the artificial structure of the synthetic data: it does not transfer to real data. A negative but informative result — a credible classifier needs real, multi-subject annotated components.

## Slide 12
PHASE 4
Downstream analysis: the cleaned signal is usable
Power per frequency band over time (spectrogram) on the clean signal — Python reproduction of the Assignment Part 3 MATLAB code.
PROOF OF USE
Output directly usable for scientific analyses.
QUALITY CHECK
Transient spikes would betray an artifact residual not captured by ICA.
BANDS
delta · theta · alpha · beta · gamma.

## Slide 13
ASSUMED LIMITATIONS
What to write honestly in the report
!
Gradient / BCG simplified in-house AAS and OBS (not the full FASTR regularization).
!
Non-deterministic ICA structural comparison, not point by point.
!
Small N a single subject: ML not robust at this scale.
!
Synthetic → real transfer does not work; real multi-subject annotations are needed.
!
Spectral comparisons align windowing and units before any conclusion.

## Slide 14
CONCLUSION & PERSPECTIVES
An open, reproducible and rigorous pipeline
ACHIEVED
• Complete EEG-fMRI pipeline reproduced in Python (FASTR & OBS from scratch).
• Ready EEGLAB-to-Python comparison chain.
• Sound ML evaluation that unmasks over-optimism.
PERSPECTIVES
• Plug in the EEGLAB exports to quantify the equivalence.
• Manually annotate the real components.
• Aggregate several subjects for robust ML.
• Make the synthetic generator more realistic.

## Slide 15
DELIVERABLES & STACK
Thank you
DELIVERABLES
• FR & EN notebooks (executed, Protocol + Analysis boxes).
• Detailed .txt explanations (FR & EN).
• Presentation (HTML slides + PPTX) · requirements.txt.
TECHNICAL STACK
Python · MNE · mne-icalabel · scikit-learn · scipy · statsmodels · pandas · matplotlib
Fixed seeds · logged states · EEGLAB-aligned naming.
Aymen Khatrani — MIMLAB, Boğaziçi University.